REMOVING UNKNOWN PASSWORDS

Dell

Dimension P100t, P75t, P90t

DIP switch bank is located next to Memory banks.

1. Set switch No. 3 to ON position.  2. Start and down computer.  3. Reset switch to OFF.

Dimension P133v, P166v, P200v

Dimension XPS M166s, M200s

Dimension XPS P133s MT

Jumper bank is located toward front of System board, marked A, B, C, D.

1. In group A, jump pins 2-3.  2. Start and down computer.  3. Replace jumper to pins 1-2.

Dimension XPS D266

Dimension XPS T550

Single jumper is located at the front of the System board, forward of the expansion slots.

NOTE: This procedure returns all settings to defaults. Check all settings in advance. You may need to reset System Processor Speed.

1. Set jumper to pins 2-3.  2. Start computer.  It will boot directly into maintenance screen of system setup program.  3. Highlight CLEAR ALL PASSWORDS, Press ENTER, Select YES, Exit.  4. Reset jumper to pins 1-2.

Dimension XPS P166c MT

Jumper bank is located at the edge of the System board, adjacent to the CPU.

1. Set jumper F (PSWD) to pins 2-3.  2. Start computer to erase password, down computer.  3. Reset jumper to pins 1-2.

Dimension 4100

Single jumper is located forward of PCI slots.

1. Jump pins 2-3.  2. Start and down computer.  3. Reset jumper to pins 1-2.

OptiPlex GX1p, GX200

System board Jumper bank is located toward front, lower side, near Riser Board connector

Topmost jumper should be marked PSWD.

1. Remove PSWD jumper.  2. Start and down computer.  3. Replace jumper.  4. Restart computer, in BIOS Setup set Chassis Intrusion to Enabled.

OptiPlex GX100, GX110

Jumper is located near front of System board, immediately above Riser board connector

1. Remove jumper plug.  2. Start computer to erase passwords, down computer.  3. Replace jumper.  4. Restart computer, in BIOS Setup set Chassis Intrusion to Enabled.

OptiPlex GXM

Jumper bank is located at the edge of the System board, adjacent to the CPU, Second jumper from to is marked PSWD.

1. Remove jumper plug.  2. Start computer to erase passwords, down computer.  3. Replace jumper.

4. Restart computer, in BIOS Setup set Chassis Intrusion to Enabled.

OptiPlex XL 575

Jumper bank is located between Memory banks and Riser 2 slot.  Jumper is marked PSWD.

1. Remove jumper plug.  2. Start computer to erase passwords, down computer.  3. Replace jumper.  4. Restart computer, in BIOS Setup set Chassis Intrusion to Enabled.

Inspiron and Latitude Notebooks, all models

No information on resetting forgotten passwords is given for these models.  Dell recommends calling Tech Support.  Proof of identity will be required.  NOTE: See Poweredge instructions.  Good luck

Poweredge 4400, 6300

Jumper bank is located on right rear corner of System board.

1. Remove jumper plug.  2. Start computer to erase passwords, down computer.  3. Replace jumper.

Gateway

Procedure for all desktop models:

1. Move jumper to pins 2-3.  2. Start and down computer.  3. Reset jumper to pins 1-2.

E-3200

Single jumper is located near center of System board.  It is usually colored blue.

E-3400

Single jumper is located toward the rear of System board, forward of parallel port.

E-3600

Jumper is located near front panel harness and USB connectors.

E-4200

Single jumper is located between PCI slots and CMOS battery.

Solo Notebook, all models

Gateway states the following:  The password feature is very secure, with no easy way to recover a forgotten password. You must return your computer for repair. Call Client Care for instructions.

Hewlitt-Packard

Vectra models

Dip switch bank is located near top side of System board.

1. Set switch no. 3 to ON.  2. Start and down computer.  3. Reset switch to OFF.